Copyright 2013 by The American Institute of Architects (AIA)

Exclusively published and distributed by Architectural Computer Services, Inc. (ARCOM) for the AIA

SECTION 024119 - SELECTIVE DEMOLITION

Revise this Section by deleting and inserting text to meet Project-specific requirements.

This Section uses the term "Architect." Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

SUMMARY

Section Includes:

Demolition and removal of selected portions of building or structure.

Demolition and removal of selected site elements.

Salvage of existing items to be reused or recycled.

MATERIALS OWNERSHIP

Unless otherwise indicated, demolition waste becomes property of Contractor.

Historic items, relics, antiques, and similar objects including, but not limited to, cornerstones and their contents, commemorative plaques and tablets, and other items of interest or value to Owner that may be uncovered during demolition remain the property of Owner.

Carefully salvage in a manner to prevent damage and promptly return to Owner.

PREINSTALLATION MEETINGS

Predemolition Conference: Conduct conference at [Project site] <Insert location>.

INFORMATIONAL SUBMITTALS

Engineering Survey: Submit engineering survey of condition of building.

Proposed Protection Measures: Submit report, including Drawings, that indicates the measures proposed for protecting individuals and property[, for environmental protection] [, for dust control] [and] [, for noise control]. Indicate proposed locations and construction of barriers.

Schedule of selective demolition activities with starting and ending dates for each activity.

Predemolition photographs or video.

Statement of Refrigerant Recovery: Signed by refrigerant recovery technician.

CLOSEOUT SUBMITTALS

Inventory of items that have been removed and salvaged.

QUALITY ASSURANCE

Refrigerant Recovery Technician Qualifications: Certified by an EPA-approved certification program.

FIELD CONDITIONS

Owner will occupy portions of building immediately adjacent to selective demolition area. Conduct selective demolition so Owner's operations will not be disrupted.

Conditions existing at time of inspection for bidding purpose will be maintained by Owner as far as practical.

Before selective demolition, Owner will remove the following items:

<Insert items to be removed by Owner>.

Notify Architect of discrepancies between existing conditions and Drawings before proceeding with selective demolition.

Retain "Hazardous Materials" paragraph below, or remove all references to hazardous materials. Insert scope of article to include asbestos, PCBs, and other materials if required. Coordinate statements with the General and Supplementary Conditions. See "Hazardous Materials" Article in the Evaluations.

Hazardous Materials: It is not expected that hazardous materials will be encountered in the Work.

Hazardous materials will be removed by Owner before start of the Work.

Retain subparagraph below to cover instances where hazardous materials are unexpectedly found and must be remediated. See the General Conditions for additional requirements on hazardous materials.

If suspected hazardous materials are encountered, do not disturb; immediately notify Architect and Owner. Hazardous materials will be removed by Owner under a separate contract.

Storage or sale of removed items or materials on-site is not permitted.

Utility Service: Maintain existing utilities indicated to remain in service and protect them against damage during selective demolition operations.

Maintain fire-protection facilities in service during selective demolition operations.

Arrange selective demolition schedule so as not to interfere with Owner's operations.

WARRANTY

Existing Warranties: Remove, replace, patch, and repair materials and surfaces cut or damaged during selective demolition, by methods and with materials and using approved contractors so as not to void existing warranties.

PRODUCTS

PERFORMANCE REQUIREMENTS

Regulatory Requirements: Comply with governing EPA notification regulations before beginning selective demolition. Comply with hauling and disposal regulations of authorities having jurisdiction.

Standards: Comply with ASSE A10.6 and NFPA 241.

EXECUTION

EXAMINATION

Verify that utilities have been disconnected and capped before starting selective demolition operations.

Usually retain first option in first paragraph below. OSHA regulations require only that a "competent person" perform an engineering survey before building demolition begins. See Evaluations.

[Perform] [Engage a professional engineer to perform] an engineering survey of condition of building to determine whether removing any element might result in structural deficiency or unplanned collapse of any portion of structure or adjacent structures during selective building demolition operations.

Inventory and record the condition of items to be removed and salvaged.

PREPARATION

Refrigerant: Before starting demolition, remove refrigerant from mechanical equipment according to 40 CFR 82 and regulations of authorities having jurisdiction.

UTILITY SERVICES AND MECHANICAL/ELECTRICAL SYSTEMS

Existing Services/Systems to Remain: Maintain services/systems indicated to remain and protect them against damage.

Retain "Existing Services/Systems to Be Removed, Relocated, or Abandoned" Paragraph below if required. Delete if Owner arranges and performs work.

Existing Services/Systems to Be Removed, Relocated, or Abandoned: Locate, identify, disconnect, and seal or cap off utility services and mechanical/electrical systems serving areas to be selectively demolished.

Retain first subparagraph below if shutting off utilities is responsibility of Owner. Delete if it is responsibility of Contractor.

Owner will arrange to shut off indicated services/systems when requested by Contractor.

Retain first subparagraph below if shutting off utilities is responsibility of Contractor. Delete if it is responsibility of Owner.

Arrange to shut off utilities with utility companies.

If services/systems are required to be removed, relocated, or abandoned, provide temporary services/systems that bypass area of selective demolition and that maintain continuity of services/systems to other parts of building.

Disconnect, demolish, and remove fire-suppression systems, plumbing, and HVAC systems, equipment, and components indicated on Drawings to be removed.

Piping to Be Removed: Remove portion of piping indicated to be removed and cap or plug remaining piping with same or compatible piping material.

Piping to Be Abandoned in Place: Drain piping and cap or plug piping with same or compatible piping material and leave in place.

Equipment to Be Removed: Disconnect and cap services and remove equipment.

Equipment to Be Removed and Reinstalled: Disconnect and cap services and remove, clean, and store equipment; when appropriate, reinstall, reconnect, and make equipment operational.

Equipment to Be Removed and Salvaged: Disconnect and cap services and remove equipment and deliver to Owner.

Ducts to Be Removed: Remove portion of ducts indicated to be removed and plug remaining ducts with same or compatible ductwork material.

Ducts to Be Abandoned in Place: Cap or plug ducts with same or compatible ductwork material and leave in place.

PROTECTION

Revise "Temporary Protection" Paragraph below to suit Project. Delete if adequately covered in Section 015000 "Temporary Facilities and Controls."

Temporary Protection: Provide temporary barricades and other protection required to prevent injury to people and damage to adjacent buildings and facilities to remain.

Temporary Shoring: Design, provide, and maintain shoring, bracing, and structural supports as required to preserve stability and prevent movement, settlement, or collapse of construction and finishes to remain, and to prevent unexpected or uncontrolled movement or collapse of construction being demolished.

Remove temporary barricades and protections where hazards no longer exist.

SELECTIVE DEMOLITION

General: Demolish and remove existing construction only to the extent required by new construction and as indicated. Use methods required to complete the Work within limitations of governing regulations and as follows:

Neatly cut openings and holes plumb, square, and true to dimensions required. Use cutting methods least likely to damage construction to remain or adjoining construction. Use hand tools or small power tools designed for sawing or grinding, not hammering and chopping. Temporarily cover openings to remain.

Cut or drill from the exposed or finished side into concealed surfaces to avoid marring existing finished surfaces.

Do not use cutting torches until work area is cleared of flammable materials. At concealed spaces, such as duct and pipe interiors, verify condition and contents of hidden space before starting flame-cutting operations. Maintain portable fire-suppression devices during flame-cutting operations.

Maintain fire watch during and for at least <Insert number> hours after flame-cutting operations.

Locate selective demolition equipment and remove debris and materials so as not to impose excessive loads on supporting walls, floors, or framing.

Dispose of demolished items and materials promptly.[ Comply with requirements in Section 017419 "Construction Waste Management and Disposal."]

Site Access and Temporary Controls: Conduct selective demolition and debris-removal operations to ensure minimum interference with roads, streets, walks, walkways, and other adjacent occupied and used facilities.

Removed and Salvaged Items:

Clean salvaged items.

Pack or crate items after cleaning. Identify contents of containers.

Store items in a secure area until delivery to Owner.

Transport items to Owner's storage area [on-site] [off-site] [designated by Owner] [indicated on Drawings].

Protect items from damage during transport and storage.

Removed and Reinstalled Items:

Clean and repair items to functional condition adequate for intended reuse.

Pack or crate items after cleaning and repairing. Identify contents of containers.

Protect items from damage during transport and storage.

Reinstall items in locations indicated. Comply with installation requirements for new materials and equipment. Provide connections, supports, and miscellaneous materials necessary to make item functional for use indicated.

In "Existing Items to Remain" Paragraph below, option adds cost. Revise to suit Project.

Existing Items to Remain: Protect construction indicated to remain against damage and soiling during selective demolition. When permitted by Architect, items may be removed to a suitable, protected storage location during selective demolition[ and cleaned] and reinstalled in their original locations after selective demolition operations are complete.

CLEANING

Insert other specific disposal, cleanup, or removal requirements to suit Project.

Remove demolition waste materials from Project site [and dispose of them in an EPA-approved construction and demolition waste landfill acceptable to authorities having jurisdiction.] [and recycle or dispose of them according to Section 017419 "Construction Waste Management and Disposal."]

Do not allow demolished materials to accumulate on-site.

Remove and transport debris in a manner that will prevent spillage on adjacent surfaces and areas.

Coordinate first subparagraph below with use of elevators, stairs, or building entries permitted by building manager.

Remove debris from elevated portions of building by chute, hoist, or other device that will convey debris to grade level in a controlled descent.

Comply with requirements specified in Section 017419 "Construction Waste Management and Disposal."

Burning: Do not burn demolished materials.

Clean adjacent structures and improvements of dust, dirt, and debris caused by selective demolition operations. Return adjacent areas to condition existing before selective demolition operations began.

END OF SECTION 024119