Copyright 2011 by The American Institute of Architects (AIA)

Exclusively published and distributed by Architectural Computer Services, Inc. (ARCOM) for the AIA

SECTION 081416 - FLUSH WOOD DOORS

Revise this Section by deleting and inserting text to meet Project-specific requirements.

This Section uses the term "Architect." Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

SUMMARY

Section Includes:

Retain one or both subparagraphs below.

Solid-core doors with wood-veneer faces.

Solid-core doors with plastic laminate faces.

Related Requirements:

Retain subparagraphs below to cross-reference requirements Contractor might expect to find in this Section but are specified in other Sections.

Section 081113 “Hollow Metal Doors and Frames”

Section 081213 “Hollow Metal Frames”.

Section 083473.16 "Wood Sound Control Door Assemblies" for acoustic flush wood doors.

Section 088000 "Glazing" for glass view panels in flush wood doors.

Section 134900 "Radiation Protection" for lead-lined flush wood doors.

ACTION SUBMITTALS

Product Data: For each type of door.[ Include factory-finishing specifications.]

Shop Drawings: Indicate location, size, and hand of each door; elevation of each kind of door; construction details not covered in Product Data; and the following:

Dimensions and locations of blocking.

Dimensions and locations of mortises and holes for hardware.

Dimensions and locations of cutouts.

Undercuts.

Requirements for veneer matching.

Doors to be factory finished and finish requirements.

Fire-protection ratings for fire-rated doors.

Samples: For [plastic-laminate door faces] [and] [factory-finished doors].

QUALITY ASSURANCE

Perform work in accordance with AWI Architectural Woodwork Quality Standards Illustrated, Section 1300, Premium Grade.

Finish doors in accordance with AWI Architectural Woodwork Quality Standards Illustrated, Section 1500, grades identified in schedule.

Manufacturer Qualifications: Company specializing in manufacturing the products specified in this section with minimum three years of documented experience.

Installed Fire Rated Door and Transom Panel Assembly: Conform to NFPA 80 for fire rated class as indicated.

DELIVERY, STORAGE, AND HANDLING

Package, deliver and store doors in accordance with AWI P-200, Section 1300.

Accept doors on site in manufacturer's packaging. Inspect for damage.

Protect door with resilient packaging sealed with heat shrunk plastic. Do not store in damp or wet areas; or in areas where sunlight might bleach veneer. Seal top and bottom edges with tinted sealer. Break seal on site to permit ventilation.

Store doors at site, stacked in a vertical position, spaced with a minimum of 1/4 inch space between each stacked door and on a minimum 4 inch high wood blocking.

PROJECT CONDITIONS

Coordinate the work with door opening construction, door frame and door hardware installation.

WARRANTY

Warrant door against warp or twist in excess of 1/4 inch in any face including full diagonal.  Replacement shall include finishing of new door, hardware damaged by malfunction of original door, and hanging in satisfactory operating condition. Period of warranty shall be for the life of the installation.

Include coverage for delamination of veneer, warping beyond specified installation tolerances, defective materials, and telegraphing core construction.

Chain-of-custody certification is not required for subcontractors (entities that install products) but is required for vendors unless they are simply acting as an agent of manufacturer and the sale is actually between manufacturer and Contractor or subcontractor.

PRODUCTS

See Editing Instruction No. 1 in the Evaluations for cautions about named manufacturers and products. For an explanation of options and Contractor's product selection procedures, see Section 016000 "Product Requirements."

MANUFACTURERS

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

Algoma Hardwoods, Inc.

Ampco

Assa Abloy

Construction Specialties, Inc.

Marshfield Door System, Inc.

Poncraft Door Co.

VT Industries, Inc.

FLUSH WOOD DOORS, GENERAL

Retain one standard in "Quality Standard" Paragraph below. Review retained standard and coordinate its requirements with retained options. See Evaluations.

Quality Standard: In addition to requirements specified, comply with WDMA I.S.1-A, "Architectural Wood Flush Doors".

WDMA I.S.1-A Performance Grade:

Heavy Duty unless otherwise indicated.

Extra Heavy Duty: At the following locations [and where indicated].

Retain and edit list of rooms below to suit project requirements.

Patient Room

Medication Room

Clean Supply JIT

Soiled Utility/Soiled Holding

Clean Equipment

Public Bathroom

Stair/Exit

Housekeeping

Retain "Fire-Rated Wood Doors" Paragraph below if applicable.

Fire-Rated Wood Doors: Doors complying with NFPA 80 that are listed and labeled by a qualified testing agency, for fire-protection ratings indicated, based on testing at positive pressure according to [NFPA 252] [or] [UL 10C].

Cores: Provide core specified or mineral core as needed to provide fire-protection rating indicated.

Retain "Edge Construction" Subparagraph below unless using surface-applied intumescent seals.

Edge Construction: Provide edge construction with intumescent seals concealed by outer stile. Comply with specified requirements for exposed edges.

Retain "Pairs" Subparagraph below if steel edges and astragals are unacceptable. Coordinate availability and ratings with manufacturers.

Pairs: Provide fire-retardant stiles that are listed and labeled for applications indicated without formed-steel edges and astragals. Provide stiles with concealed intumescent seals. Comply with specified requirements for exposed edges.

Retain "Smoke- and Draft-Control Door Assemblies" Paragraph below if required. The IBC requires fire door assemblies to comply with smoke- and draft-control requirements in corridors, smoke barriers, and smoke partitions.

Smoke- and Draft-Control Door Assemblies: Listed and labeled for smoke and draft control, based on testing according to UL 1784.

Retain "Particleboard-Core Doors" Paragraph below if doors have particleboard cores.

Particleboard-Core Doors:

Particleboard: ANSI A208.1, Grade LD-2, made with binder containing no urea-formaldehyde.

Blocking: Provide wood blocking in particleboard-core doors as needed to eliminate through-bolting hardware.

Provide doors with glued-wood-stave or structural-composite-lumber cores instead of particleboard cores for doors indicated to receive exit devices.

Structural-Composite-Lumber-Core Doors:

Structural Composite Lumber: WDMA I.S.10.

Screw Withdrawal, Face: 700 lbf (3100 N).

Screw Withdrawal, Edge: 400 lbf (1780 N).

Mineral-Core Doors:

Core: Noncombustible mineral product complying with requirements of referenced quality standard and testing and inspecting agency for fire-protection rating indicated.

Blocking: Provide composite blocking with improved screw-holding capability approved for use in doors of fire-protection ratings indicated as needed to eliminate through-bolting hardware.

Edge Construction: At hinge stiles, provide laminated-edge construction with improved screw-holding capability and split resistance. Comply with specified requirements for exposed edges.

VENEER-FACED DOORS FOR TRANSPARENT FINISH

See the tables at the end of the Evaluations for a list of manufacturers' products. Use these tables in combination with manufacturers' catalogs or product data to insert series, type, model, and designations of other characteristics.

Copy appropriate paragraphs below and re-edit for each product.

Insert drawing designation for each product required. Use these designations on Drawings to identify each product.

Interior Solid-Core Doors <Insert drawing designation>:

AWI's, AWMAC's, and WI's "Architectural Woodwork Standards" requires Grade AA faces for Premium-grade doors; WDMA I.S.1-A requires Grade A faces for Premium-grade doors. Both standards require Grade A faces for Custom-grade doors unless Grade B is specified. See Evaluations.

Grade: [Premium, with Grade A faces] [Custom (Grade A faces)].

Options in "Species" Subparagraph below are examples only; revise or insert another species.

Species: [Select white birch] [Cherry] [Select white maple] [Red oak] [White oak] [Walnut] [match existing] <Insert species>.

"Rift cut" option in "Cut" Subparagraph below applies only to oak.

Cut: [Rotary cut] [Plain sliced (flat sliced)] [Quarter sliced] [Rift cut] [match existing].

"Pleasing" option in "Match between Veneer Leaves" Subparagraph below is available only with Grade B veneers.

Match between Veneer Leaves: [Book] [Slip] [Pleasing] match.

"Center-balance" option in "Assembly of Veneer Leaves on Door Faces" Subparagraph below is expensive. AWI's, AWMAC's, and WI's "Architectural Woodwork Standards" requires center-balance match for Premium-grade doors. "Running" option is standard for Custom-grade and WDMA Premium-grade doors. See Evaluations.

Assembly of Veneer Leaves on Door Faces: [Center-balance] [Balance] [Running] match.

Pair and Set Match: Provide for doors hung in same opening[ or separated only by mullions].

Retain one of five options in "Core" Subparagraph below.

Core: [Particleboard] [Structural composite lumber].

Construction: [Five] [Seven] plies. Stiles and rails are bonded to core, then entire unit is abrasive planed before veneering. Faces are bonded to core using a hot press.

PLASTIC-LAMINATE-FACED DOORS

See the tables at the end of the Evaluations for a list of manufacturers' products. Use these tables in combination with manufacturers' catalogs or product data to insert series, type, model, and designations of other characteristics.

Copy appropriate paragraphs below and re-edit for each product.

Insert drawing designation for each product required. Use these designations on Drawings to identify each product.

Interior Solid-Core Doors <Insert drawing designation>:

Grade: [Premium] [Custom].

Plastic-Laminate Faces: High-pressure decorative laminates complying with NEMA LD 3, Grade HGS.

Revise "Colors, Patterns, and Finishes" Subparagraph below to indicate color, pattern, and finish if preselected.

Colors, Patterns, and Finishes: [As indicated] [As selected by Architect from laminate manufacturer's full range of products].

Exposed Vertical Edges: 3 mil. PVC edge protection to match plastic laminate.

Core: [Particleboard] [Structural composite lumber].

Retain one of four options in "Core" Subparagraph above and one of two "Construction" subparagraphs below. Glued-wood-stave core is only allowed with five-ply construction. See Evaluations.

Construction: Five plies. Stiles and rails are bonded to core, then entire unit is abrasive planed before faces and crossbands are applied.  Faces are bonded to core using a hot press.

LIGHT FRAMES AND LOUVERS

Retain "Wood-Veneered Beads for Light Openings in Fire-Rated Doors" or "Metal Frames for Light Openings in Fire-Rated Doors" Paragraph below if required for doors with fire-protection rating exceeding 20 minutes.

Wood-Veneered Beads for Light Openings in Fire-Rated Doors: Manufacturer's standard wood-veneered noncombustible beads matching veneer species of door faces and approved for use in doors of fire-protection rating indicated. Include concealed metal glazing clips where required for opening size and fire-protection rating indicated.

Metal Frames for Light Openings in Fire-Rated Doors: Manufacturer's standard frame formed of 0.048-inch- (1.2-mm-) thick, cold-rolled steel sheet; [factory primed for paint] [with baked-enamel- or powder-coated] finish; and approved for use in doors of fire-protection rating indicated.

Metal Louvers:

<Double click here to find, evaluate, and insert list of manufacturers and products.>

Retain one of three "Metal and Finish" subparagraphs below.

Metal and Finish: Hot-dip galvanized steel, 0.040 inch (1.0 mm) thick, [factory primed for paint] [with baked-enamel- or powder-coated] finish.

Metal and Finish: Extruded aluminum with Class II, clear anodic finish, AA-M12C22A31.

Metal and Finish: Extruded aluminum with [light bronze] [medium bronze] [dark bronze] [black], Class II, color anodic finish, AA-M12C22A32/A34.

FABRICATION

Delete first paragraph below if no doors are required to be factory fitted. Retain paragraph and revise to indicate exceptions if only some doors are required to be factory fitted. Plastic-laminate-edged and factory-finished doors must be factory fitted and machined. Fire-rated and plastic-laminate-faced doors with wood edges should also be factory fitted and machined. Factory fitting and machining for other doors are optional. See Evaluations.

Factory fit doors to suit frame-opening sizes indicated. Comply with clearance requirements of referenced quality standard for fitting unless otherwise indicated.

Comply with NFPA 80 requirements for fire-rated doors.

Delete first paragraph below if no doors are required to be factory machined. Retain paragraph and revise to indicate exceptions if only some doors are required to be factory machined. See Evaluations.

Factory machine doors for hardware that is not surface applied.

Openings: Factory cut and trim openings through doors.

Light Openings: Trim openings with moldings of material and profile indicated.

"Glazing" Subparagraph below is unnecessary if using only metal light frames.

Glazing: Factory install glazing in doors indicated to be factory finished. Comply with applicable requirements in Section 088000 "Glazing."

Louvers: Factory install louvers in prepared openings.

FACTORY FINISHING

Retain this article if factory finishing is required. Factory finishing can be used to help comply with LEED-NC, LEED-CS, or LEED-CI Credit IEQ 4.2, which limits VOC content of paints and coatings used within buildings. Factory finishing also has other advantages. See Evaluations.

General: Comply with referenced quality standard for factory finishing. Complete fabrication, including fitting doors for openings and machining for hardware that is not surface applied, before finishing.

Finish faces, all four edges, edges of cutouts, and mortises. Stains and fillers may be omitted on[ top and] bottom edges, edges of cutouts, and mortises.

Factory finish doors that are indicated to receive transparent finish.

Transparent Finish:

In "Grade" Subparagraph below, usually retain same grade for finish as specified for doors.

Grade: [Premium] [Custom].

Finish: [WDMA TR-4 conversion varnish] [or] [WDMA TR-6 catalyzed polyurethane] <Insert finish designation>.

Staining: [Match Architect's sample] [Match existing] [As selected by Architect from manufacturer's full range] [None required].

Retain one of three options in "Staining" Subparagraph above and usually one of three options in "Effect" Subparagraph below. Some door manufacturers will not provide filled finish because filling is best done by hand, which cannot be done on a finishing line; instead, some will offer semifilled finish as described below. Delete subparagraph below if using only closed-grain wood species.

Effect: [Open-grain finish] [Filled finish] [Semifilled finish, produced by applying an additional finish coat to partially fill the wood pores].

Retain one of two options in "Sheen" Subparagraph below or revise to suit Project.

Sheen: [Satin] [Semigloss].

EXECUTION

INSTALLATION

Hardware: For installation, see [Section 087100 "Door Hardware."] [Section 087111 "Door Hardware (Descriptive Specification)."]

Installation Instructions: Install doors to comply with manufacturer's written instructions and referenced quality standard, and as indicated.

Retain first subparagraph below for fire-rated doors.

Install fire-rated doors according to NFPA 80.

Retain subparagraph below for smoke- and draft-control doors. The IBC requires fire door assemblies to comply with smoke- and draft-control requirements in corridors, smoke barriers, and smoke partitions.

Install smoke- and draft-control doors according to NFPA 105.

Retain "Job-Fitted Doors" Paragraph below if all doors are not factory fitted. Factory fitting of fire-rated doors is preferred to job fitting because of limitations on trimming narrower stiles and rails.

Job-Fitted Doors: Align and fit doors in frames with uniform clearances and bevels as indicated below; do not trim stiles and rails in excess of limits set by manufacturer or permitted for fire-rated doors. Machine doors for hardware. Seal edges of doors, edges of cutouts, and mortises after fitting and machining.

Clearances: Provide 1/8 inch (3.2 mm) at heads, jambs, and between pairs of doors. Provide 1/8 inch (3.2 mm) from bottom of door to top of decorative floor finish or covering unless otherwise indicated. Where threshold is shown or scheduled, provide 1/4 inch (6.4 mm) from bottom of door to top of threshold unless otherwise indicated.

Retain subparagraph below for fire-rated doors or if doors are not factory fitted.

Comply with NFPA 80 for fire-rated doors.

Factory-Fitted Doors: Align in frames for uniform clearance at each edge.

Factory-Finished Doors: Restore finish before installation if fitting or machining is required at Project site.

END OF SECTION 081416