Copyright 2011 by The American Institute of Architects (AIA)

Exclusively published and distributed by Architectural Computer Services, Inc. (ARCOM) for the AIA

SECTION 064116 - PLASTIC-LAMINATE-FACED ARCHITECTURAL CABINETS

Revise this Section by deleting and inserting text to meet Project-specific requirements.

This Section uses the term "Architect." Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

Before editing this Section, review requirements of the Architectural Woodwork Institute (AWI), Architectural Woodwork Manufacturers Association of Canada (AWMAC), and Woodwork Institute's (WI) "Architectural Woodwork Standards." This review helps to avoid repeating or conflicting with requirements of that standard.

GENERAL

SUMMARY

Section Includes:

Plastic-laminate-faced architectural cabinets.

Wood furring, blocking, shims, and hanging strips for installing plastic-laminate-faced architectural cabinets unless concealed within other construction before cabinet installation.

Related Requirements:

Retain subparagraph below to cross-reference requirements Contractor might expect to find in this Section but are specified in other Sections.

Section 123623.13 "Plastic-Laminate-Clad Countertops."

ACTION SUBMITTALS

Shop Drawings: Show location of each item, dimensioned plans and elevations, large-scale details, attachment devices, and other components.

Samples:

Delete items in subparagraphs below that are not needed for control of grain character, color, and finish, or insert other items. The "Architectural Woodwork Standards" require samples to be "as wide as practical" by 12 inches (300 mm) for lumber and 12 by 12 inches (300 by 300 mm) for panel products.

Plastic laminates, for each color, pattern, and surface finish.

Thermoset decorative panels, for each color, pattern, and surface finish.

FIELD CONDITIONS

Environmental Limitations: Do not deliver or install cabinets until building is enclosed, wet work is complete, and HVAC system is operating and maintaining temperature and relative humidity at occupancy levels during the remainder of the construction period.

PRODUCTS

See Editing Instruction No. 1 in the Evaluations for cautions about named manufacturers and products. For an explanation of options and Contractor's product selection procedures, see Section 016000 "Product Requirements."

PLASTIC-LAMINATE-FACED ARCHITECTURAL CABINETS

Quality Standard: Unless otherwise indicated, comply with the "Architectural Woodwork Standards" for grades of architectural plastic-laminate cabinets indicated for construction, finishes, installation, and other requirements.

Grade: Premium.

Type of Construction: [Frameless] [Face frame].

Cabinet, Door, and Drawer Front Interface Style: Flush overlay.

High-Pressure Decorative Laminate: NEMA LD 3, grades as indicated or if not indicated, as required by woodwork quality standard.

Laminate Cladding for Exposed Surfaces:

Retain grade designations from options in first four subparagraphs below. Grade HGS is 1.2 mm (0.048 inch) thick, Grades HGL and HGP are 1.0 mm (0.039 inch) thick, and Grade VGS is 0.7 mm (0.028 inch) thick.

Horizontal Surfaces: Grade HGS.

Postformed Surfaces: Grade HGP.

Vertical Surfaces: [Grade HGS] [Grade VGS].

Pattern Direction: Vertically for drawer fronts, doors, and fixed panels.

Delete "Materials for Semiexposed Surfaces" Paragraph below for woodworker's option from choices in standard.

Materials for Semiexposed Surfaces:

Surfaces Other Than Drawer Bodies: High-pressure decorative laminate, NEMA LD 3, Grade CLS.

Drawer Sides and Backs: Thermoset decorative panels with PVC edge banding.

Drawer Bottoms: Thermoset decorative panels.

Retain "Dust Panels" Paragraph below if required. Dust panels are not required by standards.

Dust Panels: 1/4-inch (6.4-mm) plywood or tempered hardboard above compartments and drawers unless located directly under tops.

Colors, Patterns, and Finishes: Provide materials and products that result in colors and textures of exposed laminate surfaces complying with the following requirements:

Retain one of three subparagraphs below. If retaining first, indicate colors, patterns, and finishes in a separate schedule.

As indicated by laminate manufacturer's designations.

Match Architect's sample.

As selected by Architect from laminate manufacturer's full range in the following categories:

Solid colors, [gloss] [matte] finish.

Solid colors with core same color as surface, [gloss] [matte] finish.

Wood grains, [gloss] [matte] finish.

Patterns, [gloss] [matte] finish.

WOOD MATERIALS

Wood Products: Provide materials that comply with requirements of referenced quality standard for each type of woodwork and quality grade specified unless otherwise indicated.

Retain one of three ranges of moisture content in "Wood Moisture Content" Subparagraph below. First range applies to Ontario, Quebec, and most of U.S. Second applies to damp coastal areas of southern U.S. and to the Maritime Provinces. Third applies to dry southwestern U.S. and to Alberta, Manitoba, and Saskatchewan. See relative-humidity and moisture-content map in the "Architectural Woodwork Standards." Note that some areas have micro-climates that differ from the surrounding region.

Wood Moisture Content: 5 to 10 percent.

Composite Wood Products: Provide materials that comply with requirements of referenced quality standard for each type of woodwork and quality grade specified unless otherwise indicated.

Retain "Recycled Content of Medium-Density Fiberboard and Particleboard" Subparagraph below if recycled content is required for LEED Credit MR 4. Recycled content of medium-density fiberboard and particleboard varies greatly; consult manufacturers before inserting requirement.

Retain "Composite Wood and Agrifiber Products" Subparagraph below if required for LEED for Schools Credit IEQ 4.4.

If retaining "Particleboard" Subparagraph below and low-emitting materials are required for LEED-NC, LEED-CI, or LEED-CS Credit IEQ 4.4, retain option for binder containing no urea formaldehyde or option requiring exterior-type glue. Specifying products without urea formaldehyde or with exterior-type glue will decrease competition and may increase costs. ANSI A208.1 requires products to comply with formaldehyde emission limits established by HUD.

Particleboard: ANSI A208.1, Grade M-2, made with binder containing no urea formaldehyde.

Softwood Plywood: DOC PS 1.

Note that the term "plywood" in "Veneer-Faced Panel Products (Hardwood Plywood)" Subparagraph below refers to a wood-based panel with veneers applied to both faces; core may be made up of veneers (either hardwood or softwood), particleboard, medium-density fiberboard, hardboard, or glued-up lumber. Retain option prohibiting urea formaldehyde if required for LEED-NC, LEED-CI, or LEED-CS Credit IEQ 4.4.

Thermoset decorative panels are frequently called "melamine." If retaining "Thermoset Decorative Panels" Subparagraph below, also retain "Medium-Density Fiberboard" and "Particleboard" subparagraphs above.

Thermoset Decorative Panels: Particleboard finished with thermally fused, melamine-impregnated decorative paper and complying with requirements of NEMA LD 3, Grade VGL, for test methods 3.3, 3.4, 3.6, 3.8, and 3.10.

FIRE-RETARDANT-TREATED MATERIALS

If fire-retardant materials are required, verify requirements and acceptability of various materials with authorities having jurisdiction.

Fire-Retardant-Treated Materials, General: Where fire-retardant-treated materials are indicated, use materials complying with requirements in this article that are acceptable to authorities having jurisdiction and with fire-test-response characteristics specified as determined by testing identical products per test method indicated by a qualified testing agency.

Identify fire-retardant-treated materials with appropriate classification marking of qualified testing agency in the form of removable paper label or imprint on surfaces that will be concealed from view after installation.

Fire-Retardant-Treated Lumber and Plywood: Products with a flame-spread index of 25 or less when tested according to ASTM E 84, with no evidence of significant progressive combustion when the test is extended an additional 20 minutes, and with the flame front not extending more than 10.5 feet (3.2 m) beyond the centerline of the burners at any time during the test.

Kiln dry lumber and plywood after treatment to a maximum moisture content of 19 and 15 percent, respectively.

CABINET HARDWARE AND ACCESSORIES

Where close matching of cabinet hardware and door hardware is required, it may be preferable to specify cabinet hardware in Section 087111 "Door Hardware (Descriptive Specification)."

General: Provide cabinet hardware and accessory materials associated with architectural cabinets except for items specified in Section 087111 "Door Hardware (Descriptive Specification)."

Paragraphs below describing hardware items are examples only; revise to suit Project. Delete if schedule is included on Drawings. See the "Architectural Woodwork Standards" or BHMA standards for illustrations of and designations for additional types of cabinet hardware.

Hinges in "Frameless Concealed Hinges (European Type)" Paragraph below are not as strong as heavy-duty butt hinges above.

Frameless Concealed Hinges (European Type): BHMA A156.9, B01602, [100] [135] [170] degrees of opening, self-closing.

Back-Mounted Pulls: BHMA A156.9, B02011.

Wire Pulls: Back mounted, solid metal, [4 inches (100 mm) long, 5/16 inch (8 mm) in diameter] [5 inches (127 mm) long, 2-1/2 inches (63.5 mm) deep, and 5/16 inch (8 mm) in diameter].

First option in "Adjustable Shelf Standards and Supports" Paragraph below specifies standards and clip-type rests for mounting at ends of shelves; second specifies standards and knife-type brackets for mounting at rear of shelves.

Adjustable Shelf Standards and Supports: [BHMA A156.9, B04071; with shelf rests, B04081] [BHMA A156.9, B04102; with shelf brackets, B04112].

Shelf rests in "Shelf Rests" Paragraph below are installed in holes drilled in cabinet sides and partitions.

Shelf Rests: BHMA A156.9, B04013; metal, two-pin type with shelf hold-down clip.

Drawer Slides: BHMA A156.9.

Grade 1 and Grade 2: Side mounted and extending under bottom edge of drawer]; full-extension type; zinc-plated steel with polymer rollers.

Grade 1HD-100 and Grade 1HD-200: Side mounted; full-extension type; zinc-plated-steel ball-bearing slides.

Grades in five subparagraphs below correspond to the following initial load test requirements: Grade 2, 30 lbf (13.3 kg); Grade 1, 50 lbf (22.2 kg); Grade 1HD-100, 100 lbf (44.5 kg); Grade 1HD-200, 200 lbf (90 kg).

For drawers not more than 3 inches (75 mm) high and not more than 24 inches (600 mm) wide, provide Grade 2.

For drawers more than 3 inches (75 mm) high but not more than 6 inches (150 mm) high and not more than 24 inches (600 mm) wide, provide Grade 1.

For drawers more than 6 inches (150 mm) high or more than 24 inches (600 mm) wide, provide Grade 1HD-100.

Locks specified in "Door Locks" and "Drawer Locks" paragraphs below are deadbolt locks, surface mounted on inside of door or drawer with only the cylinder exposed on outside; revise either paragraph if another type of lock is required.

Door Locks: BHMA A156.11, E07121.

Drawer Locks: BHMA A156.11, E07041.

Door and Drawer Silencers: BHMA A156.16, L03011.

Retain "Float Glass for Cabinet Doors" or "Tempered Float Glass for Cabinet Doors" Paragraph below if glass is required for cabinet doors. Retain option in second paragraph for seamed exposed edges if unframed glass doors are used.

Exposed Hardware Finishes: For exposed hardware, provide finish that complies with BHMA A156.18 for BHMA finish number indicated.

Subparagraphs below are examples only. Revise to suit Project. If more than one finish is required, indicate location of each here or on Drawings. See Evaluations.

Dark, Oxidized, Satin Bronze, Oil Rubbed: BHMA 613 for bronze base; BHMA 640 for steel base; match Architect's sample.

Bright Brass, Clear Coated: BHMA 605 for brass base; BHMA 632 for steel base.

Bright Brass, Vacuum Coated: BHMA 723 for brass base; BHMA 729 for zinc-coated-steel base.

Satin Brass, Blackened, Bright Relieved, Clear Coated: BHMA 610 for brass base; BHMA 636 for steel base.

Satin Chromium Plated: BHMA 626 for brass or bronze base; BHMA 652 for steel base.

Bright Chromium Plated: BHMA 625 for brass or bronze base; BHMA 651 for steel base.

Satin Stainless Steel: BHMA 630.

MISCELLANEOUS MATERIALS

Furring, Blocking, Shims, and Hanging Strips: [Softwood or hardwood lumber] [Fire-retardant-treated softwood lumber], kiln dried to less than 15 percent moisture content.

Anchors: Select material, type, size, and finish required for each substrate for secure anchorage. Provide metal expansion sleeves or expansion bolts for post-installed anchors. Use nonferrous-metal or hot-dip galvanized anchors and inserts at inside face of exterior walls and at floors.

Retain first "Adhesives" Paragraph below if required for LEED-NC, LEED-CI, and LEED-CS Credit IEQ 4.4. See Evaluations.

Adhesives: Do not use adhesives that contain urea formaldehyde.

Retain "Adhesives" Paragraph below if required for LEED for Schools.

Adhesives: Use adhesives that meet the testing and product requirements of the California Department of Health Services' "Standard Practice for the Testing of Volatile Organic Emissions from Various Sources Using Small-Scale Environmental Chambers."

Retain one of five options in "Adhesive for Bonding Plastic Laminate" Paragraph below or delete all and leave as woodworker's option. First and second options are suitable for general use and for postforming. Use only unpigmented product with through-color laminate. Water-based varieties must be used where VOC limits apply. Third option is white or yellow wood glue and is good for use with through-color laminates; it is not for postforming and has poor water, chemical, and heat resistance. Fourth option has good water and chemical resistance and resistance to temperature fluctuations; it is also suitable for postforming and for through-color laminates. Retain fifth option if required for fire resistance; it is the only adhesive with flame-spread index less than 25. Resorcinol also has good water and chemical resistance; it is not for postforming or for through-color laminates.

Adhesive for Bonding Plastic Laminate: [Unpigmented contact cement] [Contact cement].

FABRICATION

Complete fabrication, including assembly and hardware application, to maximum extent possible before shipment to Project site. Disassemble components only as necessary for shipment and installation. Where necessary for fitting at site, provide ample allowance for scribing, trimming, and fitting.

Shop-cut openings to maximum extent possible to receive hardware, appliances, electrical work, and similar items. Locate openings accurately and use templates or roughing-in diagrams to produce accurately sized and shaped openings. Sand edges of cutouts to remove splinters and burrs.

Install glass to comply with applicable requirements in Section 088000 "Glazing" and in GANA's "Glazing Manual." For glass in wood frames, secure glass with removable stops.

EXECUTION

PREPARATION

Before installation, condition cabinets to average prevailing humidity conditions in installation areas.

INSTALLATION

Revise "Grade" Paragraph below if installation grade is different from fabrication grade.

Grade: Install cabinets to comply with same grade as item to be installed.

Install cabinets level, plumb, true, and straight. Shim as required with concealed shims. Install level and plumb to a tolerance of 1/8 inch in 96 inches (3 mm in 2400 mm).

Scribe and cut cabinets to fit adjoining work, refinish cut surfaces, and repair damaged finish at cuts.

Anchor cabinets to anchors or blocking built in or directly attached to substrates. Secure with countersunk, concealed fasteners and blind nailing. Use fine finishing nails[ or finishing screws] for exposed fastening, countersunk and filled flush with woodwork.

Cabinets: Install without distortion so doors and drawers fit openings properly and are accurately aligned. Adjust hardware to center doors and drawers in openings and to provide unencumbered operation. Complete installation of hardware and accessory items as indicated.

Install cabinets with no more than 1/8 inch in 96-inch (3 mm in 2400-mm) sag, bow, or other variation from a straight line.

Revise requirements in subparagraph below as necessary for seismic restraint of cabinets. Delete if hanging cleats are used and are detailed on Drawings.

Fasten wall cabinets through back, near top and bottom, and at ends not more than 16 inches (400 mm) o.c. with [No. 10 wafer-head screws sized for not less than 1-1/2-inch (38-mm) penetration into wood framing, blocking, or hanging strips] [No. 10 wafer-head sheet metal screws through metal backing or metal framing behind wall finish] [toggle bolts through metal backing or metal framing behind wall finish].

END OF SECTION 064116